## Slide 1
RGB
Enemy AI System
State-based multi-agent AI in Unreal Engine 5.7
Arena coordination • Adaptive pressure • Specialized movement
Notes: This presentation explains the current enemy AI in RGB. The system combines an arena-level coordinator with autonomous enemy actors. The newest part is arena-driven pressure tuning, where puzzle progress changes selected AI attributes while the encounter is running.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (overview and arena-driven pressure profiles).

## Slide 2
AI COORDINATION
The AI design problem
02
Multiple enemies should create pressure without creating chaos
Distinct behavior for each enemy type
One shared limit for simultaneous attacks
Readable telegraphs and reliable hit checks
PLAYER
ATTACK
PRESSURE
FLY
PATROL
Notes: The design problem is coordination. Independent enemies tend to stack on the player or attack together. RGB keeps individual enemy behavior, but uses shared rules so the group stays readable and fair.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (overview and coordination).

## Slide 3
SYSTEM STRUCTURE
Two-level AI architecture
03
GROUP LEVEL
Arena Control
Progress, profiles, lifecycle
Coordinator component
Eligibility, roles, shared attack budget
LOCAL LEVEL
Ground enemy
Patrol and melee
Teleporter
Utility-scored points
Flying enemy
Weighted steering
Notes: The architecture has two decision levels. Arena Control owns progress, tuning and lifecycle. Its coordinator component makes group decisions such as who may attack. Each enemy actor then executes its own local behavior. This is centralized coordination with decentralized execution.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (sections 1 and 4, plus arena-driven pressure profiles).

## Slide 4
ADAPTIVE AI
Arena progress drives enemy pressure
04
Puzzle completion becomes an AI input
0%
100%
FRGBProgressValue
Coordination
Maximum attackers
Ground
Patrol, chase, detection
Teleporter and flying
Timing, scoring, steering
Endpoints interpolate linearly or through an optional response curve
Losing puzzle progress also reduces the evaluated pressure
Notes: This is the main new system. Arena completion is normalized from zero to one. Each FRGBProgressValue contains a value at no progress, a value near completion and an optional response curve. Arena Control evaluates those profiles and applies the result to coordination and each enemy type. If puzzle progress drops, the pressure values drop as well. This is a good point to begin the live demo.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (arena-driven pressure profiles).

## Slide 5
MULTI-AGENT COORDINATION
Shared attack budget
05
All enemy types compete for the same attack slots
GROUND
TELEPORT
FLYING
Threat eligibility
Sight, range, level, active state
ATTACK
BUDGET
Selected attacker
Permission is released after execution
Ready attacks first · committed roles next · distance last
A lower budget blocks new attacks but does not cancel an attack already running
Notes: The coordinator first filters enemies by threat eligibility. Ground enemies need suitable ground, sight and a locally clear direction. Flyers need sight. Teleporters need the same combat level, horizontal range and no active teleport. Ready attacks receive priority, followed by committed roles and distance. If progress lowers the budget, attacks already running may finish.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (arena-driven pressure profiles, coordination).

## Slide 6
STATE-BASED BEHAVIOR
Ground enemy
06
Random patrol and visibility-based pursuit
PATROL
Random direction
Wall and ledge probes
VISIBLE
Range, height
and line of sight
CHASE
Preference and
chase speed profile
ATTACK
Montage starts
immediately
AttackHitDelay defines the damage moment
Progress changes cooldown, not animation rate or hit timing
Notes: The ground enemy uses explicit action states and collision queries. Patrol direction changes at random intervals, while wall and ledge probes keep movement safe. Pursuit requires range, similar height and line of sight. There is no separate attack preparation delay now. The montage starts immediately, and the authored AttackHitDelay remains the damage moment.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (ground profile and sections 5–6).

## Slide 7
UTILITY-BASED SELECTION
Teleporter enemy
07
Arena-owned points are filtered, scored and reserved
PLAYER
REJECT
RESERVED
VALID
VALID
1 FILTER
Occupied, repeated, outside arena
2 SCORE
Random value + danger near player
3 RESERVE
Charge, revalidate, then move
AoE trigger: same level + horizontal range
Damage still requires the actual X/Z AoE radius
Notes: With arena tuning enabled, Arena Control owns the teleporter's Target Points. The enemy filters invalid destinations, scores the rest using randomness and danger near the player, reserves the winner and validates it again after the charge. The AoE can only start on the same combat level and within horizontal range. Damage still requires the real X/Z AoE radius.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (teleporter profile and section 8).

## Slide 8
STEERING BEHAVIOR
Flying enemy
08
Weighted steering creates the desired velocity
PURSUIT
Direction to player
SEPARATION
Avoid nearby enemies
AVOIDANCE
Probe clear directions
DESIRED
VELOCITY
SAFE MOVEMENT
Acceleration, sweep, slide, camera clamp
Progress profiles can change speed, acceleration and steering weights
Notes: The flyer combines pursuit, separation and obstacle avoidance into a desired direction. It accelerates toward the desired velocity, uses collision sweeps and slides along surfaces. Arena profiles can adjust speed, acceleration, tracking, separation and probe distance as progress changes. The camera zone still constrains the full capsule.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (flying profile and section 7).

## Slide 9
GAMEPLAY INTEGRATION
Combat and enemy lifecycle
09
Events connect AI, color rules and respawning
MATCHING HIT
DISABLED
COLOR TRANSFER
INACTIVE INSTANCE
RESTORED
The arena reuses the authored enemy instance
Transform, Blueprint tuning, color options and arena ownership are preserved
Respawn delay may also scale with arena progress
Notes: A matching color hit reduces health. Elimination switches the enemy to Disabled, releases shared permissions and broadcasts an event. A grounded enemy can transfer color to its platform. The arena now hides and deactivates the configured actor, then restores that same instance later. This preserves placed and Blueprint-specific settings across respawn and reset.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (sections 9–10 and arena lifecycle changes).

## Slide 10
ENGINEERING DECISION
AI method choice
10
Deterministic C++ matched the project scope
CURRENT SYSTEM
Explicit states
Timers and collision queries
Repeatable debugging
UNREAL-MAP OPTION
Multi-agent reinforcement learning
External Python training pipeline
UE 4.27 integration target
Chosen
Future research
The implemented system remains directly tunable inside Unreal
Notes: Unreal-MAP was considered as a multi-agent reinforcement-learning workflow. It could support automated training, but RGB would need observations, actions, rewards, episode reset and an external Python pipeline. The current deterministic C++ system was already working and remained easier to debug and tune within the available scope.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (section 15).

## Slide 11
PROJECT STATUS
Verification and current limits
11
5 AUTOMATION TESTS PASSED
Progress curves
Teleport scoring and range
Shared attack budget
Lifecycle configuration
Inactive damage guards
VISUAL PIE CHECKS PENDING
Movement tuning
Animation synchronization
Two-arena setup
Pressure balancing
Current limits
No global platform pathfinding · no puzzle-aware sabotage · local flyer avoidance
The result is a modular AI foundation with explicit, testable behavior
Notes: The updated RGB.ArenaAI automation suite passed five tests with no failures or skips. Those tests cover deterministic rules and lifecycle regressions. The documentation also records that visual PIE verification is still pending for movement feel, animation timing, two-arena wiring and final pressure tuning. Current design limits include no global platform navigation and no puzzle-aware sabotage decisions.
Source: ENEMY_AI_SYSTEM_EXPLAINED.txt (AI coordination test checklist and section 13).